## Slide 1: City of Houston Water System
Nooreen Jilani, P.E.
City of Houston
Public Works & Engineering
Infrastructure Planning
October 04, 2012
Notes: Lots of ways to think about Houston’s water
Deliver annual average of 400 MGD
of water (Max. 672 MGD)
Service 470,000 customer accounts
  1,162,720 connections
  2,940,000 residents
Maintain 7,480 miles of water lines
54,000 Fire Hydrants
150,000 Valves

## Slide 3
70 % of the earth is comprised of water but out of this only 2.5 % is fresh water
Out of this 2.5 %
only 1 % is
available for humans and
ecosystem

## Slide 4
State Water Planning Regions
Houston and suburbs are in Region H

## Slide 5: City of Houston Water System
Lisa Lattu, PE & AICP
City of Houston Public Works & Engineering
Infrastructure Planning
September 16, 2011
Downtown Houston
Texas Medical Center Houston
Notes: Lots of ways to think about Houston’s water
Deliver annual average of 400 MGD
of water (Max. 672 MGD)
Service 470,000 customer accounts
  1,162,720 connections
  2,940,000 residents
Maintain 7,480 miles of water lines
54,000 Fire Hydrants
150,000 Valves

## Slide 6
Energy Corridor
Galleria

## Slide 7
Houston is nation’s fourth largest City
Houston has no geographical boundaries to limit expansion
It is a challenge to plan, built, maintain and manage the water system to meet Houston’s
ever increasing needs
Challenges we face

## Slide 8: Components of Water Planning
Water Sources and Rights
(Supply)
Conveyance System
(Raw Water)
Transmission and Distribution
(Treated Water)
Treatment and Pressurizing
(Plants and Re-Pump Stations)
Demands
(Customers)

## Slide 9: Today’s Water Sources
Lake Conroe 1973
Dam on San Jacinto River
Lake Livingston 1969
Dam on Trinity River
Trinity River
Lake Houston 1954
Dam on San Jacinto River
Ground Water
Wells

## Slide 10
Surface Water Sources

## Slide 11
Coastal Water Authority Water Conveyance Canals
Notes: MAIN CANAL 22 miles clay lined gravity flow with a gradient of .9 ft per mile
Normal water surface width of 100 Ft.
Normal Water Depth is14 Ft.
Capacity: Exceeds 1.3 Billion Gallons/Day
TRINITY RIVER PUMP STATION
Ultimate Pumping Units: 18 Vertical Pumps
  Ultimate Capacity (Gallons/Day) 1.4 Billion
Existing Pumping Units: 16 Vertical Pumps
Existing Capacity (Gallons/Day)
  1.3 Billion total with all 16 pumps
  1.0 Billion with 3 Large pumps on Stand-by.

## Slide 12
East Water Purification Plant
350 MGD (Million gallon per day)
Southeast Water Purification Plant
200 MGD (Million gallon per day)
Northeast Water Purification Plant 80 MGD (Million gallon per day)
Treatment Plants

## Slide 13
New, Small, North East Surface Water Plant
Original,
Large, East Surface Water Plant
Medium, South East Surface Water Plant
Major Roads
Re-pressurization Locations
Water Treatment and Transmission System

## Slide 14: Southwest Re-pump Station

## Slide 15: Water Supply and Demand
San Jacinto River Basin
Lake Conroe 60 MGD (Million gallon per day)
Lake Houston 163 MGD
with an additional 36 MGD Run of River
Bayou & Reuse permits 634 MGD With environmental flows dedication
Trinity River Basin
Lake Livingston 806 MGD
Wallisville 34 MGD
Barbers Hill Canal 40 MGD
Dayton Canal 34 MGD
Brazos River
Allens Creek 62 MGD In Planning
Total Permitted Water Rights 1,869 MGD
Available Groundwater 235 MGD (Per Local Regulations)
City of Houston Annual Average Demand is 400 mgd and Peak Demand is 672 mgd
Total Annual Average Demand = 400 mgd+ 350 mgd (Suburbs)+ 240 mgd (Industry)

## Slide 16: Water Customers
Commercial
Industrial
Houston
Citizens
Local
Cities &
Villages
Local
Cities
Large
Industrial
Strategic
Partners
(Water Authorities)
SE Plant
Participants
Municipal
Utility
Districts
(MUD’s)
Water
Resources
Treated Water Customers
Untreated Water Customers

## Slide 17
Strategic Partner-Customers

## Slide 19
Subsidence:
Is the motion of the Earth's surface as it shifts downward relative to a datum such as sea-level
1940 benchmark re-leveling results show that Baytown area has subsided 3.2 feet and Texas City Area has subsided 1.6 feet
Detailed research by Houston Chamber of commerce
in 1947 showed that excessive pumping of ground
water is the major cause of subsidence
Harris Galveston Subsidence district was established in
1975 to regulate and limit pumping in Harris and
Galveston counties by issuing ground water permits

## Slide 20
Area I 90%
Area II 80%
Area III
  30% by 2010
  70% by 2020
  80% by 2030
Surface water
Conversion Requirements
Area 3
Area 2
Area 1
Harris-Galveston Subsidence District Surface Water Conversion Plan
2011 Surface Water Conversion
Area I: 100%
Area II: 93.1%
Area III: 49.51%

## Slide 21
Lake Houston Reservoir Level 2011

## Slide 23
Luce Bayou Project

## Slide 24
Future Water Supply Projects
Allens Creek Reservoir

## Slide 26: City of Houston works diligently to meet the ever-growing water needs
Planning with its continuous efforts make sure that City has enough resources and capacity in the system to meet the existing and future demands
Engineering and Construction manage the building of
new water infrastructure
Operations and maintenance groups work hard to ensure that all the facilities are running adequately for uninterrupted supply to the citizens
Water quality groups do sampling, testing and cross connection control to maintain and improve the water quality through their continuous surveillance.

## Slide 28
Drinking
Water
Groundwater
Rain/Storm
Water
Recycled
Water
Wastewater
ONE
WATER
Notes: 28
Doug Walters, P.E.
LA Sanitation

## Slide 29
Thank you
Questions?